# Text boxes

ITEM：EP21655

CENTRIFUGE

OWNER’S  MANUAL

Ⅰ.Outline of uses:

Special features following: It is beautiful in appearance. Large in capacity but small in bulk and has a complete function and a stable performance, you can chose the speed that you need at the setrange, and it can keep balance automaticly, in addition, it has a little rate of increase in temperature and can be used efficiently and widely. It is a dependable instrument for qualitative analysis of serum, plasma and immunity in hospitals or chemical and biochemical laboratories.

Ⅱ.Technical data

| Model | Max. Speed (r/min) | Capacity | Max. rcf (xg) | Fix time (min) | Power Supply | Dimensions (CM) | Weight (Kg) | power |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 800 □ | 4000 | 20ml×6 | 1790 | / | 110V-120V ~60HZ | 29*29*26 | 5 | 25W |
| 800D/ 800-1□ |  |  | 1790 | 0-60 |  | 29*29*26 | 5 | 25W |
| 80-1 □ |  | 20ml×6 | 1790 | 0-120 |  | 32*30*27 | 6 | 25W |
| 80-2 □ |  | 20ml×12 | 2325 |  |  | 37*33*31 | 9 | 40W |
| 90-1 □ | 5000 | 20ml×12 | 2950 |  |  | 38*37*33 | 12 | 90W |
| 90-2 □ |  | 15 ml×12 | 2950 |  |  | 38*37*33 | 12 | 90W |
| TGL-16 (A) □ | 16000 | 1.5ml×12 0.5ml×12 | 17000 |  |  | 37*33*31 | 8 | 250W |