TL32755 WIRE STRIPPER MACHINE

This machine is easily to use, portable,energy saving and good looks,just like the normal stripper machine usage.

Wire range: Φ1.5mm~ 25mm

measure.: 240*320*320MM

power: 0.18kw

weight:13kg

1：    plastic regulating nut

2：    blades regulating nut

3：    motor

4：    feeding panel

5：    blades fixed screw

6：    feeding hole

7：     reducer casing

8：    shaft

9：    blades

10：   switch

manual

1: adjust distance between blades and shaft in  accordance with the cable size(the insulating layer stripped but not hurt the inner conductor)

2: feeding: strip the cables through feeding hole( u can adjust the feeding hole according cable size to the proper position which  cables can enter into but not swing)

3: stripping: (hand operated) rotate hand crank in order to peeling, if can’t peel:

- too small wire diameter

- the blades center not in line with groove center( adjust the blades core)

- blades edge is too dull( sharpen the blades)

Notice: don’t input your hands into the machine in any circumstance